## Slide 1: Egress Window Existing Residential Occupancies
(These slides include animated explanations. You must play the slide show from the beginning to see the animations.)

## Slide 2
Height
At least 20”
Width
At least 20”
Minimum
648 in2
Double Hung
Height x Width = Area
Example: 648 sq.in. required opening size divided by 20 inch minimum width equals 32.4 inches in height to be code compliant

## Slide 3
Height
At least 20”
Width
At least 20”
Minimum
648 in2
Sliding
Height x Width = Area
Example: 648 sq.in. required opening size divided by 40 inch height equals 16.2 inches in width, but shall be 20 inches to be code compliant

## Slide 4
Height
At least 20”
Width
At least 20”
Minimum
648 in2
Casement
Height x Width = Area
Example: 648 sq.in. required opening size divided by 24 inch width equals 27 inches in height and is code compliant

## Slide 5
Casement
Cutaway View
BOTH the rough window opening AND the clearance left by the open window MUST be no less than 20” in width.
Width
No less than 20”

## Slide 6
Height from bottom of opening to floor
Maximum of 48”
≤ 48”
≤ 48”
> 48”

## Slide 7
Window Well
Minimum 1296 in2

## Slide 8
Window Well
A
at least 36”
B
at least 36”
D
at least 36”
W
at least 36”
Minimum 1296 in2
Depth x Width = Area
Example: 1296 sq.in. required window well divided by 48 inch width equals 27 inch depth, but minimum depth is 36 inches to be code compliant

## Slide 9
≤ 44”
Window Well
Vertical Depth
No ladder required if the well vertical depth is equal to or less than 44”

## Slide 10
> 44”
Window Well
Vertical Depth
If the well vertical depth is greater than 44”, a ladder is required for egress